Voltage	2010-09-15

1A = {1C over 1s} newline newline q(t_2) - q(t_1) = int_{t_1}^{t_2} i dt

Assume we have charge moving through a circuit element. Further assume work is involved in moving the charge.

U is potential energy.

Voltage (or potential difference) is the amount of work required per unit of positive charge to move the charge through a circuit element.
{V_a - V_b} underbrace {V_{ab}} > {U_a - U_b} over q newline 1V = 1J over 1C

Since voltage is a difference, we need a convention to distinguish points of high potential and low potential. We will use polarity marks.

Power and Energy

If there is a voltage drop, energy must be absorbed by the element.

The rate of absorption of energy by the element is power. P(t) = v(t)i(t). 1W = 1VA